## Slide 1: Basic of Networking
VishwanaTH m s
VISHWACLOUDLAB.com

## Slide 2: ISO/OSI Reference Model

## Slide 3: Layered Packet Format

## Slide 4: Major Concepts in Network
Same Network – Switch
Different Network -- Router
PC – Traffic Generator
  Switch and Router DOES NOT generate Traffic, they only manage it
IP Address – Its an tool used by PC for sending packets from Source to Destination

## Slide 5: Network Diagram
Router
10.0.0.1/8
172.100.0.1/16
SW01
SW02
IP Add: 10.40.30.20
Subnet: 255.0.0.0
GW : 10.0.0.1
IP Add: 10.80.10.30
Subnet: 255.0.0.0
GW : 10.0.0.1
IP Add: 172.100.10.30
Subnet: 255.255.0.0
GW : 172.100.0.1
IP Add: 172.100.20.40
Subnet: 255.255.0.0
GW : 172.100.0.1

## Slide 6: Basic Networking continued…..
Two types of IP address
IPv4 – 32 bit
IPV6 – 128 bit
IPv4 address format
X .X .X .X
8bit 8bit 8bit 8bit
1st Octet 2nd Octet 3rd Octet 4th Octet
00000000.00000000.00000000.00000000
Binary to Decimal Conversation
0000 0000  0 – Min Value
1111 1111  255 – Max Value

## Slide 7: Binary to Decimal Conversion & ViceVersa
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1
Eg1: - 1*128 + 0*64 + 0*32 + 1*16 + 0*8 + 0*4 + 0*2 + 1*1  128+16+1 = 145
Eg2: - 1 1 1 0 0 0 1 1  128+64+32+2+1 = 227
Eg3: - 1 1 0 0 1 1 0 0  ???
Eg4: - 1 0 1 0 1 0 1 0  ???
Find Decimal value of below Binary octets
Eg1: - 10010001
Eg2: - 1110001 1

## Slide 8: IP address V4
An IP address is a 32-bit address and are unique.
The address space of IPv4 is 2^32 or 4,294,967,296.

## Slide 9: IP Address IPV4
CLASS A – 0.0.0.0 to 127.255.255.255 --- USED FOR PUBLIC NETWORK, UNICAST TRAFFIC
CLASS B – 128.0.0.0 to 191.255.255.255 --- USED FOR PUBLIC NETWORK, UNICAST TRAFFIC
CLASS C – 192.0.0.0 to 223.255.255.255 --- USED FOR PUBLIC NETWORK, UNICAST TRAFFIC
CLASS D – 224.0.0.0 to 239.255.255.255 --- USED FOR MULTICAST
CLASS E – 240.0.0.0 to 255.255.255.255 --- USED FOR RESEARCH
Class A - 00000000 to 01111111
Class B - 10000000 to 10111111
Class C - 11000000 to 11011111
Class D - 11100000 to 11101111
Class E - 11110000 to 11111111

## Slide 10: IP Address Classes
RFC 791 defines the IP protocol.
Note: -- The valid addresses in class A start from 1 to 126. Network 0.0.0.0 is defined for use as
a broadcast address and 127.0.0.0 is reserved for use as loopback address.

## Slide 11: Default Subnet Mask
Class A – 255.0.0.0 – 11111111.00000000.00000000.00000000 -- /8
Class B – 255.255.0.0 – 11111111. 11111111.00000000.00000000 -- /16
Class C – 255.255.255.0 – 11111111. 11111111. 11111111.00000000 -- /24
CLASS A – 0.0.0.0 to 127.255.255.255 --- USED FOR PUBLIC NETWORK, UNICAST TRAFFIC
CLASS B – 128.0.0.0 to 191.255.255.255 --- USED FOR PUBLIC NETWORK, UNICAST TRAFFIC
CLASS C – 192.0.0.0 to 223.255.255.255 --- USED FOR PUBLIC NETWORK, UNICAST TRAFFIC
CLASS D – 224.0.0.0 to 239.255.255.255 --- USED FOR MULTICAST
CLASS E – 240.0.0.0 to 255.255.255.255 --- USED FOR RESEARCH

## Slide 12: Roles of Router, Switch and PC
  Router  Determines the path to the different destination Network
  Switch  Transports the traffic from SRC and DST on same network on HIGH SPEED
  PC  Determines whether the SRC IP and DST IP are SAME or DIFFERENT network.
SRC – Source
DST -- Destination

## Slide 13: PC determines whether Src IP and Dst Ip are in same or Diff network
PC does an “BINARY AND” operation between
SRC IP BINARY AND SRC SUBNETMASK
&
DST IP BINARY AND SRC SUBNETMASK
0 AND 0 = 0
0 AND 1 = 0
1 AND 0 = 0
1 AND 1 = 1

## Slide 14: PC - Operations
Example:1 Src IP – 10.40.30.20 and Dst IP – 10.80.10.30
Src IP AND Src SubnetMask
00001010. 00101000.00011110.00010100  10.40.30.20 – Src IP
11111111. 00000000.00000000.00000000  255.0.0.0 -- Src Subnet mask
00001010. 00000000.00000000.00000000  10.0.0.0
10.0.0.0/8 is the Network ID for “10.40.30.20”
DST IP AND Src SubnetMask
00001010. 01010000.00001010.00011110  10.80.10.30 – DST IP
11111111. 00000000.00000000.00000000  255.0.0.0 -- SRC Subnet Mask
00001010. 00000000.00000000.00000000  10.0.0.0  Result
10.0.0.0/8 is the Network ID for “10.80.10.30”
AND
AND
0 AND 0 = 0
0 AND 1 = 0
1 AND 0 = 0
1 AND 1 = 1

## Slide 15: CONCLUSION of AND operation:
Since the network ID’s of the SRC IP and DST IP are the same they are in the same network.

## Slide 16: Traffic flow for Same Network
PC1: Requests for MAC ID of the PC2 to the switch
SW01: Does an Broadcast for the first time only
PC2: Replies to the broadcast with its MAC ID
SW01: passess the info to PC1
PC1: Send data to PC2.
PC2: Replies to the data to PC1

## Slide 17: PC - Operations
Example:2 Src IP – 10.40.30.20 and Dst IP – 11.81.11.31
Src IP AND Src SubnetMask
00001010. 00101000.00011110.00010100 – 10.40.30.20
11111111. 00000000.00000000.00000000 – 255.0.0.0
00001010. 00000000.00000000.00000000 – 10.0.0.0
Statement  10.0.0.0/8 is the Network ID for “10.40.30.20”
DST IP AND Src SubnetMask
00001011. 01010001.00001011.00011111 – 11.81.11.31
11111111. 00000000.00000000.00000000 – 255.0.0.0
00001011. 00000000.00000000.00000000 – 11.0.0.0
Statement  11.0.0.0/8 is the Network ID for “11.81.11.31”
Results:
The Network ID’s are different, so they are in different network.

## Slide 18: PC - Operations
Example:3 Src IP – 10.40.30.20 and Dst IP – 172.100.10.30
Src IP AND Src SubnetMask
00001010. 00101000.00011110.00010100  10.40.30.20
11111111. 00000000.00000000.00000000  255.0.0.0
00001010. 00000000.00000000.00000000  10.0.0.0
10.0.0.0/8 is the Network ID for “10.40.30.20”
DST IP AND Src SubnetMask
10101100. 01100100.00001010.00011110  172.100.10.30
11111111. 00000000.00000000.00000000  255.0.0.0
10101100. 00000000.00000000.00000000  172.0.0.0/8
172.0.0.0/8 is the Network ID for “172.100.10.30”
Results:
The Network ID’s are different, so they are in different network.

## Slide 19: PC – Operations – Example -4
Example:4 Src IP 172.100.10.30 and DST IP – 192.168.25.20
Since the SRC ip is Class B , we have to consider Class B subnet mask
Source
172.100.10.30  SRC IP
255.255.0.0  SRC Subnet Mask
--------------------
172.100.0.0/16
Destination
192.168.25.20  DST IP
255.255.0.0  SRC Subnet Mask
--------------------
192.168.0.0/16

## Slide 20: Traffic flow for Different Network
PC1: Requests for MAC ID of the default Router(Default Gateway)
SW01: Does Broadcast for the first time to get the MAC ID of the Router interface
RT: Replies to the Broadcast with its MAC ID
SW01: Replies to the PC1 with MAC ID of the Router
PC1: Send’s Packet to RT to forward it to the DST network (PC3)
RT: Checks the Routing Table for the forwarding of the packet.
RT: Sends an Broadcast request to the switch (SW02) to get
the MAC ID of the PC3 for first time
PC3: replies the Broadcast
RT: Forwards the request to the PC3.

## Slide 21: Netid and Hostid
In classful addressing, an IP address in class A, B and C is divided into two parts netid and hostid. These parts are varying length, depending on the class of the address.

## Slide 22: Conclusion of the AND operation
If the 1st Octet in CLASS A is same for both SRC IP and DST IP , then they are in the same network, if not they are in Different Network.
If the 1st & 2nd Octet in CLASS B is same for both SRC IP and DST IP , then they are in the same network, if not they are in Different Network.
If the 1st, 2nd & 3rd Octet in CLASS C is same for both SRC IP and DST IP , then they are in the same network, if not they are in Different Network.

## Slide 23: Some Example
20.30.40.50 & 20.20.30.10 -- ?????
They are in the CLASS-A network and the 1st octet is same, means they are in the same N/W.
200.30.10.10 & 200.31.10.20 -- ????
They are in Class-c and the 1st 3 Byte is NOT same. – Diff Network
150.140.130.120 & 150.140.120.130 -- ????
They are in the Class-B and 1st 2 Octet are SAME. Hence they are in same Network

## Slide 24: First and Last Usable IP & Broadcast IP
Src IP AND Src SubnetMask -- 10.40.30.20 AND 255.0.0.0
00001010. 00101000.00011110.00010100
11111111. 00000000.00000000.00000000
00001010. 00000000.00000000.00000000
10.0.0.0/8 is the Network ID for “10.40.30.20”
First IP –NW ID 00001010.00000000.00000000.00000000 – 10.0.0.0
First Usable IP  00001010.00000000.00000000.00000001 – 10.0.0.1
Last Usable IP  00001010.11111111.11111111.11111110 – 10.255.255.254
Broadcast IP  00001010.11111111.11111111.11111111 – 10.255.255.255

## Slide 25: Summary

## Slide 26: Problem
Scenario 1 .
Customer 1 wants 5000 IP’s in a single network
Customer 2 wants 10000 IP’s in a single network

## Slide 27: Number of Networks and Hosts Per each Network
CLASS A ---- NNNNNNNN.HHHHHHHH.HHHHHHHH.HHHHHHHH
Subnet Mask - 255 . 0 . 0 . 0
28= 0-126 224= 16,777,216
CLASS B ---- NNNNNNNN.NNNNNNNN.HHHHHHHH.HHHHHHHH
SubnetMask - 255 . 255 . 0 . 0
216= (128-191)*256 = 16K 216= 65,536
CLASS C ---- NNNNNNNN.NNNNNNNN.NNNNNNNN.HHHHHHHH
subnetMask - 255 . 255 . 255 . 0
224= (192-223)*256*256 = 2M 28= 256
H == HOST == IP ADDRESS == VM == Laptop == Desktop

## Slide 28: Solution to the Problem
Scenario 1 .
Customer 1 wants 5000 IP’s in a single network
Customer 2 wants 10000 IP’s in a single network
Solution.
Provide each Customer with a CLASS B network.
140.140.0.0/16
140.141.0.0/16

## Slide 29: Problem Due to IPV4 Classes
  In networking world, if we need to control traffic , it can be done in an controlled way Between DIFFERENT NETWORK.
  It’s very very TOUGH to control traffic within the same network.
  Means Class A and B are having huge Amount of HOSTS in each network, and we would start wasting IP’s by assign each network to individual Customers.
  Solution to this Problem is “SUBNETTING”