## Slide 1: Networking – IPv6-Address
VishwanaTH m s
VISHWACLOUDLAB.COM

## Slide 2: Introduction of IPV6
  Internet Protocol Version 6(IPv6) is the latest revision of the Internet Protocol, the communication protocol that provides an identification and location system for computers on networks and routes traffic across the internet.
  IPv6 was developed by IETF to deal with the long-anticipated problem of IPv4 address exhaustion.
  IPv6 was intended to replace IPv4, which still carries the vast majority of Internet traffic.
  In contrast to IPv4, which defined an IP address as a 32-bit value, IPv6 addresses have a size of 128 bits. Therefore, IPv6 has a vastly enlarged address space compared to IPv4.

## Slide 3: Features of IPV6
  New Header Format
  Large Address Space
  Efficient and Hierarchical addressing and routing infrastructure
  Stateless and stateful address configuration
  Built-in Security
  Better support for Quality of Service
  New support for neighboring node interaction
  Extensibility

## Slide 4: IPV6 Addressing
The number of possible address in IPv6 is 2^128(3.4*10^38) addresses.
340,282,366,920,938,463,463,374,607,431,768,211,456 to be exact.
Such a large amount of available IP addresses ensure that we will never again run out of IP addresses.

## Slide 5: IPV6 Addressing
  The IPv6 address size is 128-bit which is represented in hexadecimals.
  The 128-bit address is divided into 16-bits, and each 16-bit block is converted into 4- digit hexadecimal number and separated by colons. This type o f representation is called colon hexadecimal.
  The format o f IPv6 address is
  xxxx: xxxx: xxxx: xxxx: xxxx: xxxx: xxxx: xxxx
  where each X is a hexadecimal representing 4 bits or a nibble.
  IPv6 address range from
  0000:0000:0000:0000:0000:0000:0000:0000 to ffff: ffff: ffff: ffff: ffff: ffff: ffff: ffff.

## Slide 6: IPV6 Addressing
IPV6 is an 128 Bit Address
Its an HEXA Decimal Values.
2600:ABCD:EF01:0000:0000:ABCD:EF01:2345  IPv6 Example.
Each digit is an HEXA Decimal number. And has “4” bits.
2600 representing in Binary  0010 0110 0000 0000
Points.
If the Address is starting with “2” then its an public IPV6 address.
If the Address is starting with “FE80” then its an LINK-Local IPV6 address
HexaDecimal -- Binary
0 -- 0000
1 -- 0001
2 -- 0010
3 -- 0011
.
.
9 -- 1001
A -- 1010
B -- 1011
C -- 1100
.
F -- 1111

## Slide 7: IPV6 Addressing
IPv6 address can be simplified by following two methods :
Omit Leading Zeros
For Example, 4FDE:0000:0000:0002:0022:F376:FF3B:AC99
may be written as 4FDE:0:0:2:22:F376:FF3B:AC99.
Eg2 -- 4FDE:0000:0000:0002:0022:F376:0000:AC99
4FDE:0:0:2:22:F376:0:AC99.

## Slide 8: IPV6 Addressing
IPv6 address can be simplified by following two methods :
Double Colon
For Example, 4FDE:0000:0000:0002:0022:F376:FF3B:AC99 can be further simplified as
4FDE::2:22:F376:FF3B:AC99.
Eg2:-- 4FDE:0000:0000:0000:0022:F376:FF3B:AC99
Can be written as -- 4FDE::22:F376:FF3B:AC99.
Eg3:-- 4FDE:0000:0000:0022:F376:0000:0000:AC99
Can be written as -- 4FDE::22:F376:0:0:AC99.
Or --- 4FDE:0:0:22:F376::AC99.

## Slide 9: Reserved Ranges of IPV6
FF00::/8 – Multicast IPV6 range
2000::/8 – Public IPV6 range
FE80::/12 – Link Local IPV6 Range
FD00::/10 – Private IPV6 range.

## Slide 10: IPV6 Addressing
  Subnetting concepts remain the same as IPV4
  There is NO concept of PATTING as have lots of IP addresses that can be spared in IPV6.
  BUT NATTING concept exists for HIDDING the server.

## Slide 11: IPV6 Address -- Subnetting
Given Main CIDR network
2600:1f18:60e1:d300::/96
Also be represented as 2600:1f18:60e1:d300:0:0::/96
Means 96 bit are network bit’s and remaining 32 are Host bits
H = 128 -96 = 32 bits
Requirement for subnetting
We need 1000 ips per network and we need 50 networks

## Slide 12: IPV6 Address -- Subnetting
Solution:
1000 ~ 2^10
But since we have lots of IPV6, we would round off the binary's to 4 bits at a time.
Either we can say – New H Bits = 12 bits or even 16 bits for our easy.
Which means  New N Bits = 128 - 16 = 112
The First Subnetwork  2600:1f18:60e1:d300:0:0:0000::/112
Second Subnetwork  2600:1f18:60e1:d300:0:0:0001::/112
Third Subnetwork  2600:1f18:60e1:d300:0:0:0002::/112

## Slide 13
This is the 7th 16bit set in the previous example, which would keep increasing by binary “1” to get the next subnetwork.
0000 0000 0000 0000  0000  0
0000 0000 0000 0001  0001  1
0000 0000 0000 0010  0002  2
0000 0000 0000 0011  0003  3
……
0000 0000 1111 0100  00F4  F4
……
0000 1111 0000 0101  0F05  F05
….
1111 1111 1111 1111  FFFF

## Slide 14: IPV4 V/S IPV6
IPv4 | IPv6
32- bit length. | 128-bit length
IPSec support is only optional. | Inbuilt IPSec support
Fragmentation is done by sender and forwarding routers | Fragmentation is only done by sender
No packet flow identification | Packet flow identification is available using flow label field
Checksum field is available in header | No checksum field in header
Option fields are available in header. | No option fields, but extension headers are available.
Broadcast messages are possible | Broadcast messages are not possible.

## Slide 15: IPv6 on AWS
Example -- 2600:1f18:60e1:d3 00::/56 – VPC CIDR Ipv6 Public /56 is Network and Host Bits are –> 128 -56 = 72 bits , means 2^72 number of HOSTs can be created in this network. For every Subnet in the VPC 2600:1f18:60e1:d300000000::/64 – First Subnet for IPV6 2600:1f18:60e1:d300000001::/64 2600:1f18:60e1:d300000010::/64 2600:1f18:60e1:d300000011::/64 2600:1f18:60e1:d31111 1111::/64  2600:1f18:60e1:d3 FF::/64 – Last IPv6 Subnetwork that can be used.

## Slide 16: More Reference Links on IPV6
https://www.mediawiki.org/wiki/Help:Range_blocks/IPv6
https://www.iana.org/assignments/ipv6-address-space/ipv6-address-space.xhtml