## Slide 1: Networking -- Subnetting
VISHWANATH M S
VISHWACLOUDLAB.COM

## Slide 2: Subnetting
Formulas for Subnetting
Since Total IPV4 bit = 32bit == Network Bits + Host Bits
Network bits = 32 – Host bits
Host bits = 32 – Network bits
For
Class A 🡪 N bit == 8 and H bit == 24
Class B 🡪 N bit == 16 and H bit == 16
Class C 🡪 N bit == 24 and H bit == 8

## Slide 3: Formula’s for Binary Numbers
2^1 = 2
2^2 = 4
2^3 = 8
2^4 = 16
2^5 = 32
2^6 = 64
2^7 = 128
2^8 =256
2^9 = 512
2^10 = 1024
2^11 = 2048
2^12 = 4096
2^13 = 8192
2^14 = 16384
2^15 = 32768
2^16 = 65536
BINARY ADDITION
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1
BINARY to Decimal Conversion Formula
2 power table

## Slide 4: Netid and Hostid with Default CLASS
In classful addressing, an IP address in class A, B and C is divided into two parts netid and hostid. These parts are varying length, depending on the class of the address.

## Slide 5: Requirement
A customer has 6 Departments.
Customer wants to control the traffic between these Departments.
Each department should have min capability of 1000 computer/users which would cater the growth for next 10 years
The Admin is suppose create subnets by using “172.18.0.0/16” main network.

## Slide 6: Requirement
Router
SW01
PC01
PC1001
SW02
SW03
PC2001
DEP01
Subnet01
SW04
PC3001
SW05
PC4001
SW06
PC5001
DEP02
Subnet02
DEP03
Subnet03
DEP04
Subnet04
DEP05
Subnet05
DEP06
Subnet06

## Slide 7: Subnetting - Examples
Subnetting – Example – 172.18.0.0/16 1000 IP’s per Sub-network, 6 Sub-Network.
Given is a Class B network which means
N bit =16, and H = 32-16 bit = 16 bits that is 65536 (2^16) IP’s by Default
where in 16 bits are for HOST ID.
But we need to break this network into smaller networks with 1000 IP’s (Hosts) in each Sub-Network.

## Slide 8: Subnetting – Example – 172.18.0.0/16 1000 IP’s per network, 6 Network
Solution:
2^10 ~ 1000, Means ,
New No. of H bits = 10 ,
New No. of N bits = 32 (Total no of IPV4 bits) – 10(H Bit) = 22.
So, the First Subnetwork is 🡪 172.18.0.0/22
To find next sub network , we need to add binary “1” to the last bit of the NEW Network bits.
Example - 1
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 9: Host IP’s in each subnetwork
172.18. 0000 0000 .00000000/22 🡪 172.18.0.0/22 – 1st Subnetwork
172.18. 0000 0000 .00000000 🡪 172.18.0.0 -- Network ID
172.18. 0000 0000 .00000001 🡪 172.18.0.1 -- First usable IP
172.18. 0000 0000 .11111111 🡪 172.18.0.255 -- usable IP
172.18. 0000 0001 .00000000 🡪 172.18.1.0 -- usable IP
172.18. 0000 0001 .11111111 🡪 172.18.1.255 -- usable IP
172.18. 0000 0010 .00000000 🡪 172.18.2.0 -- usable IP
172.18. 0000 0010 .11111111 🡪 172.18.2.255 -- usable IP
172.18. 0000 0011 .00000000 🡪 172.18.3.0 -- usable IP
172.18. 0000 0011 .11111110 🡪 172.18.3.254 -- Last usable IP
172.18. 0000 0011 .11111111 🡪 172.18.3.255 -- Broadcast IP
Example - 1
Network Part
Host Part

## Slide 10: Subnetting – Example – 172.18.0.0/16 1000 IP’s per network, 6 Network
Solution Continued …
In our example it would be“22” bit for Network and we need add BINARY “1” at 22nd bit.
172.18. 0000 0000 .00000000/22 🡪 172.18.0.0/22 – 1st Subnetwork
  +1
172.18. 0000 0100 .00000000/22 🡪 172.18.4.0/22 – 2nd Subnetwork
  +1
172.18. 0000 1000 .00000000/22 🡪 172.18.8.0/22 – 3rd Subnetwork
  +1
172.18. 0000 1100 .00000000/22 🡪 172.18.12.0/22 – 4th Subnetwork
  +1
172.18. 0001 0000 .00000000/22 🡪 172.18.16.0/22 – 5th Subnetwork
  :
  :
  :
172.18. 1111 11 00 .00000000/22 🡪 172.18.252.0/22 – Last Subnetwork
Example - 1
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10
Octets Range
1st – 1 – 8
2nd – 9 – 16
3rd – 17 – 24
4th – 25 - 32

## Slide 11: Host IP’s in each subnetwork
172.18. 0000 0000 .0/22 🡪 172.18.0.0/22 – 1st Subnetwork
172.18. 0000 0000 .0 🡪 172.18.0.0 -- Network ID – First IP
172.18. 0000 0000 .00000001 🡪 172.18.0.1 -- First usable IP
172.18. 0000 0011 .11111110 🡪 172.18.3.254 -- Last usable IP
172.18. 0000 0011 .11111111 🡪 172.18.3.255 -- Broadcast IP – Last IP
172.18. 0000 0100 .0/22 🡪 172.18.4.0/22 – 2nd Subnetwork
172.18. 0000 0100 .0 🡪 172.18.4.0 -- Network ID – First IP
172.18. 0000 0100 .00000001 🡪 172.18.4.1 -- First usable IP
172.18. 0000 0111 .11111110 🡪 172.18.7.254 -- Last usable IP
172.18. 0000 0111 .11111111 🡪 172.18.7.255 -- Broadcast IP – Last IP
172.18. 0000 1000 .0/22 🡪 172.18.8.0/22 – 3rd Subnetwork
172.18. 0000 1000 .0 🡪 172.18.8.0 -- Network ID – First IP
172.18. 0000 1000 .00000001 🡪 172.18.8.1 -- First usable IP
172.18. 0000 1011 .11111110 🡪 172.18.11.254 -- Last usable IP
172.18. 0000 1011 .11111111 🡪 172.18.11.255 -- Broadcast IP – Last IP
Example - 1

## Slide 12: Subnetting – Example – 172.18.0.0/16 500 IP’s per network, 6 Network
2^9 ~ 500, Means , No of H bits = 9 , No of N bits = 32 – 9 = 23.
So, the First Subnetwork is 🡪 172.18.0.0/23
To find next network , we need to add binary “1” to the last bit of the Network bit.
In our example it would on the “23” bit
172.18. 0000 0000 .00000000/23 🡪 172.18.0.0/23 – 1st Subnetwork
+1
172.18. 0000 0010 . 00000000/23 🡪 172.18.2.0/23 – 2nd Subnetwork
+1
172.18. 0000 0100 . 00000000/23 🡪 172.18.4.0/23 – 3rd Subnetwork
+1
172.18. 0000 0110 . 00000000/23 🡪 172.18.6.0/23 – 4th Subnetwork
+1
172.18. 0000 1000 . 00000000/23 🡪 172.18.8.0/23
172.18. 1111 1110 . 00000000/23 🡪 172.18.254.0/23 – Last Subnetwork
Example - 2
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10

## Slide 13: Host IP’s in each subnetwork
172.18. 0000 0000 .0/23 🡪 172.18.0.0/23 – 1st Subnetwork
172.18. 0000 0000 .0 🡪 172.18.0.0 -- Network ID – First IP
172.18. 0000 0000 .00000001 🡪 172.18.0.1 -- First usable IP
172.18. 0000 0001 .11111110 🡪 172.18.1.254 -- Last usable IP
172.18. 0000 0001 .11111111 🡪 172.18.1.255 -- Broadcast IP – Last IP
172.18. 0000 0010 .0/23 🡪 172.18.2.0/23 – 2nd Subnetwork
172.18. 0000 0010 .0 🡪 172.18.2.0 -- Network ID – First IP
172.18. 0000 0010 .00000001 🡪 172.18.2.1 -- First usable IP
172.18. 0000 0011 .11111110 🡪 172.18.3.254 -- Last usable IP
172.18. 0000 0011 .11111111 🡪 172.18.3.255 -- Broadcast IP – Last IP
172.18. 0000 0100 .0/23 🡪 172.18.4.0/23 – 3rd Subnetwork
172.18. 0000 0100 .0 🡪 172.18.4.0 -- Network ID – First IP
172.18. 0000 0100 .00000001 🡪 172.18.4.1 -- First usable IP
172.18. 0000 0101 .11111110 🡪 172.18.5.254 -- Last usable IP
172.18. 0000 0101 .11111111 🡪 172.18.5.255 -- Broadcast IP – Last IP
Example - 1

## Slide 14: CIDR
The Subnetworks created on the CLASSFULL (/8, /16 or /24 Default Subnets) are called as CIDR (CLASSLESS INTERDOMAIN ROUTING ADDRESS)
12.0.0.0/8 -- CLASSFULL Network
120.120.0.0/16 – CLASSFULL NETWORK
200.200.200.0/24 – CLASSFULL Network
CIDR
Eg: -- 172.18.0.0/23 -- THE IP and the SUBNET do not match in the class
or 172.18.4.0/23

## Slide 15: Subnetting – Example – 192.168.0.0/20 200 IP’s per network, 6 Network
Solution:
200 ~ 2^8, No of new H bit = 8, No of New N bit = 32 -8 =24
192.168.0.0/24 H
192.168.0000 0000.00000000/24🡪 192.168.0.0/24 – 1st Subnetwork
+1
192.168.0000 0001.00000000/24 🡪 192.168.1.0/24 – 2nd Subnetwork
+1
192.168.0000 0010.00000000/24 🡪 192.168.2.0/24
+1
192.168.0000 0011.00000000 /24 🡪 192.168.3.0/24
+1
192.168.0000 0100.00000000/24 🡪 192.168.4.0/24
…………
192.168.0000 1111.00000000/24 🡪 192.168.15.0/24 – Last Subnetwork
Example - 3
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10

## Slide 16: Subnetting – Example – 192.168.0.0/18 60 IP’s per network, 6 Network
Solution:
60 ~ 2^6, No of new H bit = 6, No of New N bit = 32 -6 =26
192.168.0.0/26 H
192.168.00000000.00000000/26🡪 192.168.0.0/26 – 1st Subnetwork
+1
192.168.00000000.01000000/26 🡪 192.168.0.64/26 – 2nd Subnetwork
+1
192.168.00000000.10000000/26 🡪 192.168.0.128/26 – 3rd Subnetwork
+1
192.168.00000000.11000000 /26 🡪 192.168.0.192/26 – 4th Subnetwork
+1
192.168.00000001.00000000/26🡪 192.168.1.0/26 – 5th Subnetwork
+1
192.168.00000001.01000000/26🡪 192.168.1.64/26 – 6th Subnetwork
192.168.00111111.11000000/26 🡪 192.168.63.192/26 – Last Subnetwork
Example - 3
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10

## Slide 17: Subnetting – Example – 192.168.69.0/20 60 IP’s per network, 6 Network
2 Steps
1. Validation
2. Subnetting
1. Validation of the given network.
192.168.0100 0101.00000000/20
The given network is INValid, because there are binary “1” after the line (on the HOST side), in the above.
Convert it to an VALID network ID by making all binary value as “0” on the HOST part.
192.168.0100 0000.00000000/20
The VALID network ID 🡪 192.168.64.0/20
Example - 4

## Slide 18: Subnetting – Example – 192.168.64.0/20 60 IP’s per network, 6 Network
60 ~ 2^6, No of new H bit = 6, No of New N bit = 32 -6 =26
192.168.64.0/26 H
192.168.0100 0000.0000 0000/26 🡪 192.168.64.0/26 – 1st Subnetwork
+1
192.168.0100 0000.0100 0000/26 🡪 192.168.64.64/26 – 2nd Subnetwork
+1
192.168.0100 0000.1000 0000/26 🡪 192.168.64.128/26
+1
192.168.0100 0000.1100 0000/26 🡪 192.168.64.192/26
+1
192.168.0100 0001.0000 0000/26 🡪 192.168.65.0/26
192.168.0100 1111.1100 0000/26 🡪 192.168.79.192/26 – Last Subnetwork
Example - 4

## Slide 19: Valid the Networks
Find whether the below Networks are Valid or NOT!!!!!
10.40.30.0/18 -- ??
10.40.00 011110 . 0/18 – INVALID Network
10.40.00 000000.0/18 🡪 10.40.0.0/18 -- NOW VALID
170.100.40.0/21 -- ??
170.100.00101 000.0/21 – 170.100.40.0/21 -- VALID NW
200.200.200.000 00000 – VALID NW
200.200.200.0/27 -- ??

## Slide 20
Subnetting – Example – 192.168.64.0/20
Given 🡪 N=20 , H = 12.
Formula 🡪 Given H bit => Total Bits required for Subnetting
60 IP’s per network, 6 Sub Network
60 Ip’s mean == 2 ^ 6 Approx – Which means we need 6 bits.
+
6 Network == 2 ^ 3 Approx – Which means we need min of 3 network bits.
Total = 6 + 3 = 9 bits (Min) Required for Satisfy the above problem, as part of the Given HOST bits.
Valid the Number of Hosts possible

## Slide 21: Subnetting – Example – 172.18.64.0/18 350 IP’s per network, 6 Network
2 Steps
1. Validation
2. Subnetting
Validation of the given network.
172.18.0100 0000.0/18
The given network is Valid, because there are no binary “1” after the line, in the above.
172.18.0101 0000.0/18 🡪 This network is not , bcz there is a binary “1” after the subnet mask (18). To make is valid, change all the binary bits to “0” after “18” (the line) bit.
Example - 5

## Slide 22: Subnetting – Example – 172.18.64.0/18 350 IP’s per network, 6 Network
350 ~ 2^9, No of new H bit= 9, no of New N bit = 32-9 =23
172.18.64.0/23
172.18.0100 0000.0/23 🡪 172.18.64.0/23 – 1st Subnetwork
+1
172.18.0100 0010.0/23 🡪 172.18.66.0/23 – 2nd Subnetwork
+1
172.18.0100 0100.0/23 🡪 172.18.68.0/23
172.18.0111111 0.0/23 🡪 172.18.126.0/23 – Last Subnetwork
In AWS – 172.18.64.0/18 – is called the VPC CIDR or Main network
In AZure – 172.18.64.0/18 – is called the VirtualNetwork address space or Main network
In GCP – 172.18.64.0/18 – is called the VPC CIDR or Main network
Example - 5
00
00

## Slide 23: Subnetting – Example – 170.170.70.0/20 100 IP’s per network, 100 Network
Solution: Valid network is 170.170.64.0/20
100 ~ 2^7, No of new H bit = 7, No of New N bit = 32 -7 =25
170.170.64.0/25 H
170.170.0100 0000.0000 0000/25🡪 170.170.64.0/25 – 1st Subnetwork
+1
170.170.0100 0000.1000 0000/25🡪 170.170.64.128/25 – 2nd Subnetwork
+1
170.170.0100 0001.0000 0000/25🡪 170.170.65.0/25 – 3rd Subnetwork
+1
170.170.0100 0000.1000 0000/25🡪 170.170.64.128/25 – 4th Subnetwork
Example - 3
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 24: Is Subnetting solution for IPV4 address shortage?
NO….
Because
We initially had total of approx. “2M” network with the “CLASS” approach
After subnetting we increase that to approx. “800M to 900M” small networks to manage the show.
But Currently we are having approx. … “25 Billion” Devices online
How do we take care of this???

## Slide 25: Is Subnetting solution for IPV4 address shortage?
To solve the Growing demand of Public IP, IPV6 is the perfect solution
But we are still in the PROCESS of migrating ALL the APPLICATIONS FROM IPV4 to IPV6, which is taking an long time (25 yrs…. And Still we are doing it).
And interim solution to work on IPV4 was to DIVIDED the IPV4 address into “PRIVATE” and “PUBLIC”.
Private IPV4
10.0.0.0 to 10.255.255.255
172.16.0.0 to 172.31.255.255
192.168.0.0 to 192.168.255.255
100.64.0.0 to 100.127.255.255

## Slide 26: NATTING and PATTING
PATTING 🡪 Converting “Many Private IP” to “one PUBLIC IP”
Means, all the traffic from “192.168.0.0/24” to the internet will use the public IP “100.100.10.21” as the IP to communicate on the INTERNET.
Note: - Any packet in the internet should have Source IP and Destination IP as PUBLIC IP.
NATTING 🡪 Converting “one Private IP” to “One Public IP”
This is used for HIDDING the Hosting servers in the
Private segment from the attacker on the internet.

## Slide 27: IPV4 Address details
Public IPV4’s range
0.0.0.0 to 9.255.255.255
11.0.0.0 to 126.255.255.255
128.0.0.0 to 169.253.255.255
169.255.255.255 to 172.15.255.255
172.32.0.0 to 192.167.255.255
192.169.0.0 to 223.255.255.255
Loopback IP
127.0.0.0 to 127.255.255.255
APIPA
169.254.0.0 to 169.254.255.255 – Used on the windows OS, as an Automatic ip address

## Slide 28: Subnet values
/17 -- 11111111.11111111.10000000.00000000 – 255.255.128.0
/18 -- 11111111.11111111.11000000.00000000 – 255.255.192.0
/19 -- 11111111.11111111.11100000.00000000 – 255.255.224.0
/20 -- 11111111.11111111.11110000.00000000 – 255.255.240.0
/21 -- 11111111.11111111.11111000.00000000 – 255.255.248.0
/22 – 11111111.11111111.11111100.00000000 – 255.255.252.0
/23 – 11111111.11111111.11111110.00000000 – 255.255.254.0
/24 – 11111111.11111111.11111111.00000000 – 255.255.255.0
2^7 2^6 2^5 2^4 2^3 2^2 2^1 2^0
128 64 32 16 8 4 2 1

## Slide 29: Subnet Pattern Match
11111111. 11111110. 00000000. 00000000 -- 255.254.0.0 -- /15
11111111. 11111111. 11111110. 00000000 -- 255.255.254.0 -- /23
11111111. 11111111. 11111111. 11111110 -- 255.255.255.254 -- /31

## Slide 30: Steps in Choosing IP address
Choose a network that can have 300 IP’s per network and we would need min of 10 networks.
Find the main CIDR
  Find the MAIN CIDR Subnet mask
  Choose the IP address range
  Validate the above IP address range
Create the Subnets

## Slide 31: Choosing your OWN Network
Choose a network that can have 300 IP’s per network and we would need min of 10 networks.
Solution:
300 ~ 2^9 = 512🡺 9 is the Host bits for every Subnetwork.
10 ~ 2^4 = 16 🡺 4 bits
Main CIDR , no of H bits == 9 + 4 == 13.
NW bit for main CIDR == 32 – H == 32 – 13 == 19
Eg: -- 192.168.33.0/19 – Here the IP is assumed
192.168.001 00001.00000000/19 – This is INVALID network,
192.168.001 00000.00000000/19 -- 192.168.32.0/19 🡪THIS IS VALID NW

## Slide 32: Subnetting – Example – 192.168.32.0/19 300 IP’s per network, 10 Network
300 ~ 2^9, No of new H bit = 9, No of New N bit = 32 - 9 =23
192.168.32.0/23 H
192.168.001 00000.0000 0000/23 🡪 192.168.32.0/23 – 1st Subnetwork
+1
192.168.001 00010.0000 0000/23 🡪 192.168.34.0/23 – 2nd Subnetwork
+1
192.168.001 00100.0000 0000/23 🡪 192.168.36.0/23
+1
192.168.001 00110.0000 0000/23 🡪 192.168.38.0/23
+1
192.168.001 01000.0000 0000/23 🡪 192.168.40.0/23
192.168.001 11110.0000 0000/23 🡪 192.168.62.0/23 – Last Subnetwork
Example - 6

## Slide 33: Choosing your OWN Network
Choose a network that can have 130 IP’s per network and we would need min of 100 networks.
Solution:
130 ~ 2^8 = 256🡺 8 is the Host bits for every Subnetwork.
100 ~ 2^7 = 128 🡺 7 bits
Main CIDR , no of H bits == 8 + 7 == 15.
NW bit for main CIDR == 32 – H == 32 – 15 == 17
Eg: -- 192.168.70.0/17 – Here the IP is assumed
192.168.010 00110.00000000/17 – This is INVALID network,
192.168.00000000.00000000/17 🡪 192.168.0.0/17 🡪VALID NW

## Slide 34: Subnetting – Example – 192.168.0.0/17 130 IP’s per network, 100 Network
130 ~ 2^8, No of new H bit = 8, No of New N bit = 32 - 8 =24
192.168.0.0/24 H
192.168.0 0000000.0000 0000/24 🡪 192.168.0.0/24 – 1st Subnetwork
+1
192.168.0 0000001.0000 0000/24 🡪 192.168.1.0/24 – 2nd Subnetwork
+1
192.168.0 0000010.0000 0000/24 🡪 192.168.2.0/24 – 3rd Subnetwork
+1
192.168.0 0000011.0000 0000/24 🡪 192.168.3.0/24 – 4th Subnetwork
+1
192.168.0 0000100.0000 0000/24 🡪 192.168.4.0/24 – 5th Subnetwork
+1
192.168.0 0000101.0000 0000/24 🡪 192.168.5.0/24 – 6th Subnetwork
………………………
192.168.011 11111.0000 0000/24 🡪 192.168.127.0/24 – Last Subnetwork
Example - 6

## Slide 35: Choosing your OWN Network
Choose a network that can have 1000 IP’s per network and we would need min of 200 networks.
Solution:
1000 ~ 2^10 = 1024🡺 10 is the Host bits for every Subnetwork.
200 ~ 2^8 = 256 🡺 8 bits
Main CIDR , no of H bits == 10 + 8 == 18.
NW bit for main CIDR == 32 – H == 32 – 18 == 14
Eg: -- 192.168.33.0/14 – Here the IP is assumed
192.10101000.00100001.0/14 – This is INVALID network,
192.168.0000000.0/14 -- 192.168.0.0/14 🡪THIS IS VALID NW

## Slide 36: Choosing your OWN Network
Choose a network that can have 60 IP’s per network and we would need min of 60 networks.
Main H bit == 6+6 =12
Main N bit = 32 -12 = 20
172.16.26.0/20 -- ???
172.16.16.0/20 – is the valid main network
Subnettnig – 172.16.16.0/20
New Subnet H bit – 6
172.16.16.0/26 – 1st
172.16.16.64/26 – 2nd
172.16.16.128/26 – 3rd
172.16.16.192/26 – 4th
172.16.

## Slide 37
172.16.0001 0000.0000 0000/26 🡪 172.16.16.0/26 – 1st Subnetwork
+1
172.16.0001 0000.0100 0000/26 🡪 172.16.16.64/26 –2nd Subnetwork
+1
172.16.0001 0000.1000 0000/26 🡪 172.16.16.128/26 – 3rd Subnetwork
+1
172.16.0001 0000.1100 0000/26 🡪 172.16.16.192/26 – 4th Subnetwork
+1
172.16.0001 0001.0000 0000/26 🡪 172.16.17.0/26 – 5th Subnetwork
+1
172.16.0001 0001.0100 0000/26 🡪 172.16.17.64/26 – 6th Subnetwork